## Slide 1
Objectives
Methods
We look to describe trends relating to how granular surfaces respond to a flexible intruder in extraterrestrial levels of gravity. This can aid in the design of probes and anchors to be used on asteroids, as well as other planetary bodies.
Probing Granular Materials in Extraterrestrial Gravity
Jack Featherstone, Karen Daniels
Photoelastic materials rotate the polarization of light depending on the local stress, which distinguishes high-stress regions from low-stress ones. The average brightness of the video frames indicates the magnitude of the instantaneous forces.
The plot to the right communicates the impending failure in the above image as a sharp drop in brightness (current time marked in blue).
To simulate the surface of a planetary body, we drive a flexible probe into a vertical layer of round, photoelastic particles at different insertion speeds and levels of gravity (Earth, Martian, Lunar, and micro) using the apparatus shown below.
We use two metrics to evaluate the activity of the granular bed:
Slipping Events: Counts the number of maxima in the time derivative of the average brightness.
Maximum Load: The maximum value of the average brightness throughout the video.
NASA’s OSIRIS-REx mission to the asteroid Bennu will likely pave the way for similar expeditions in the future, escalating the importance of efficient probe design.
Under the influence of planetary gravity, increased probe insertion speed yields fewer failure events with little increase in force magnitudes during these events.
More trials are needed to determine the specific dynamics in microgravity, but this regime appears to follow different principles than when planetary gravity is present.
Another avenue to investigate is the impact of the probe flexibility on the insertion process. The insertion speed and the probe flexibility may also be coupled, leading to more complicated dynamics.
Conclusions
Results
To run trials in Martian, Lunar, and micro gravity, the apparatus was loaded aboard a plane which flew parabolic flight paths as a part of project EMPANADA.
Office of Undergraduate Research
Photoelastic grains
Camera
Motor

## Slide 2
Objectives
Methods
Light Emission from Cell Phones: Spectrum Analysis
Ryan Branagan, Jared Kempton, Dali Sun
Conclusions
Results
This project aims to investigate the spectrum of the electroluminescence emission collected from the cell phones using an ocean-optics spectrum analyzer. The purity of the color spectrum would be analyzed using a python script, by which the color coordinates will be determined.
References
We notice that the data for cyan and green for all blue light/night mode is not entirely cyan and green and is shifted away from blue, which means that the filter is taking blue light out, and is working as advertised. The data for blue shifts more towards blue, which means that the filter is not working and will need improvements in the future.
We analyzed light at 50%, 75%, 100% brightness and with blue light/night mode on. The brightness makes no sense but with the blue light filter we see the point move away from the blue region. The purity of the color spectra was preserved and the color purity was found using the distance A/B. The purity appears to be decent.
PY 452
Color Matching Function—An overview | ScienceDirect Topics. (2020). Retrieved October 22, 2020, from https://www.sciencedirect.com/topics/engineering/color-matching-function
Measuring radiometric spectra and CIE color space of light sources with the FLAME spectro-radiometer — Spectrecology. (n.d.). Retrieved October 22, 2020, from https://www.spectrecology.com/flame-spectrometer/
Standard Solar Spectra. (n.d.). Retrieved October 23, 2020, from https://www.pveducation.org/pvcdrom/appendices/standard-solar-spectra
Wyman, Chris; Sloan, Peter-Pike; Shirley, Peter (July 12, 2013). "Simple Analytic Approximations to the CIE XYZ Color Matching Functions". Journal of Computer Graphics Techniques. 2 (2): 1-11. ISSN 2331-7418.
Wyszecki, Günter & Stiles, Walter Stanley (2000). Color Science: Concepts and Methods, Quantitative Data and Formulae (2E ed.). Wiley-Interscience. ISBN 0-471-39918-3.
To create our python script we started with simple data from the sun. We plotted this on a color map which showed the color of the sun as white; which is to be expected.
The colorful graph on the left shows the xy color space. It is bound by the spectral locus comprised of points belonging to monochromatic light, light of a single wavelength. Anything inside the boundary is a combination of various wavelengths of light. The bottom line is called the line of purples and does not have a single wavelength but is a mixture of red and blue.
In order to get an xy coordinate we need to calculate XYZ values. This is done by integrating the spectra with each color matching function. The color matching functions represent the response of the eye to different wavelengths, and are similar to the response curves of the long, medium, and short cones in the eye
The dominant and complementary wavelength are found by drawing a line between the xy coordinate and the “white point”. The white point is the point chosen to be white light
corresponding to equal intensity of all wavelengths. The boundary closest to the data point is the dominant wavelength and the other side is the complementary wavelength. To calculate the color purity we take the ratio of the distance A/B between the dominant wavelength and the white point, and the xy coordinate and the white point.
Notes: Title Idea:
Measuring a Phone Screen to Determine LED Quality

## Slide 3
In order to get an xy coordinate we need to
calculate XYZ values. This is done by
integrating the spectra with each
color matching function. The color
matching functions represent the
response of the eye to different
wavelengths, and are similar to the response
curves of the long, medium, and short cones
in the eye fffffffffffffffffffffffffffffffffffffffffffffffff
Fffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffff
Ffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffff
Ffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffff
Ffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffff
fffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffffff

## Slide 4: objectives
Measure qualities of light to determine the quality of phone screens.
This project aims to investigate the spectrum of the electroluminescence emission collected from the cell phones using an ocean-optics spectrum analyzer. The purity of the color spectrum would be analyzed using a python script, by which the color coordinates will be determined.

## Slide 5: methods
Our goal is to talk about the quality of LEDs and we can do that by analyzing the light emitted and the color of that light. The International Commission on Illumination officially adopted a color space in 1931 that can give information about how humans perceive color. *Empty color map* This graph shows the xy color space. It is bound by the spectral locus comprised of points belonging to monochromatic light (light of a single wavelength). Anything inside the boundary is a combination of various wavelengths of light. The bottom line is called the line of purples and does not have a single wavelength but is a mixture of red and blue. *Sun data* In order to get an xy coordinate we must analyze light. We will use the sun as an example. Here is the spectra of the sun, you can see that emits a wide range of wavelengths but has a peak in the visible range. *Color Matching Functions* In order to get an xy coordinate we need to calculate XYZ values. This is done by integrating the spectra with each color matching function. The color matching functions represent the response of the eye to different wavelengths, and are similar to but not the same as the response curves of the long, medium, and short cones in the eye. *sun xy example* This is the xy chromaticity coordinate for the sun plotted. We would expect the sun to be white and this is what we see. *color quality* Something we would like to know is the purity of the color as well as the dominant and complementary wavelength. To find them we draw a line between the xy coordinate and the “white point”. The white point is the point chosen to be white light corresponding to equal intensity of all wavelengths. Where the line intersects the boundary closest to the point is the dominant wavelength and the point where the line intersects on the other side is the complementary wavelength. To calculate the color purity we take the ratio of the distance between the dominant wavelength and the white point, and the xy coordinate and the white point.
1 - empty map 2 - spectral data 3 - color matching functions 4 - sun xy example 5 - color quality

## Slide 6: methods
Notes: Spectrometer pic from https://www.semanticscholar.org/paper/The-Simulation%2C-Design%2C-and-Fabrication-of-Optical-Juneau/6c27202e1eb22fc09757fb196a336a6012e07afd#extracted

## Slide 7: results
*our data* We analyzed light at 50%, 75%, 100% brightness and with blue light/night mode on. The brightness makes no sense but with the blue light filter we see the point move away from the blue region.

## Slide 8: conclusion
We notice a shift in light away from blue but the brightness is inconclusive.